## Slide 1: Buffalo River Networks-Creating a Neural Network for Predicting Water Quality from Precipitation
Riley Blasiak
CIE 500-Xudong Fan
5/5/2025

## Slide 2: Background
Buffalo’s River water quality is highly dependent on precipitation
  Runoff
  Combined Sewer Overflows
https://www.google.com/url?sa=i&url=https%3A%2F%2Fmegamanual.geosyntec.com%2Fnpsmanual%2Fsectionintrourbanstormwaterrunoff.aspx&psig=AOvVaw2wUGs7K8qJCehLzKEhkP_V&ust=1746543322747000&source=images&cd=vfe&opi=89978449&ved=0CBoQ3YkBahcKEwjA-qmLy4yNAxUAAAAAHQAAAAAQCg

## Slide 3: Data Collection
Buffalo Niagara Waterkeeper river water quality data

## Slide 4: Data Collection
NEXRAD L3 radar data-from NOAA
  For now, we used DAA data subcategory (Storm total Precipitation inch).
  Pulled a single point value for each location and each time
  Used MetPy to read these data files [1]

## Slide 5: Research Question/ Motivation
How can we develop a Neural Network to predict water quality variables from a variable that is consistent across the study area?
For this project we are using storm total precipitation as our consistent variable.
With consistent parameters and data throughout the network we can create a Graphical Neural Network for the river systems which will be useful for predicting water quality, and Combined sewer overflows.
How can we develop a Neural Network to predict water quality variables from a variable that is consistent across the study area?
  For this project we are using storm total precipitation as our consistent variable.

## Slide 6: Creating the Neural Network
Parameters of interest
Scale features and targets
Split into training and testing set
3 hidden layers with p-> 100, 100->60, 60->1 neurons using ReLU activation
Create batches to train and test model
Train model
Evaluate model performance on test set
Check unscaled predictions vs actual data
1 | Precipitation
2 | Turbidity
3 | Dissolved oxygen %
4 | Conductivity
5 | TDS
6 | Latitude
7 | Longitude
8 | Temperature

## Slide 7: Batch creation

## Slide 8: Fine Tuning the Neural Network
First, we want to determine which parameter we are predicting
Start with all other parameters are predicting the one, and cut down until accuracy stops improving
Table shows Test MSE loss
 | Features |  |  |  |  |  |  |  |  |  |  |  | 
Target | 1,2,3,4,6,7 | 1,2,3,4,6 | 1,2,3,4,7 | 1,2,3,7 | 1,2,4,7 | 1,3,4,7 | 1,4,7 | 1,4 | 4, | 1,6,7 | 1,6,7,8 | 1,6 | 1,7
TDS | 0.0744 | 0.0837 | 0.0661 | 0.9389 | 0.069 | 0.0603 | 0.0466 | 0.0398 | 0.0397 | 0.3763 | 0.5237 | 0.7195 | 0.8224
Conductivity |  |  |  |  |  |  |  |  |  | 0.4343 |  |  | 
Dissolved oxygen % |  |  |  |  |  |  |  |  |  | 0.953 |  |  | 
Turbidity |  |  |  |  |  |  |  |  |  | 0.8582 |  |  | 
1 | Precipitation
2 | Turbidity
3 | Dissolved oxygen %
4 | Conductivity
5 | TDS
6 | Latitude
7 | Longitude
8 | Temperature
 | Features |  |  |  |  |  |  |  |  |  |  |  | 
Target | 1,2,3,4,6,7 | 1,2,3,4,6 | 1,2,3,4,7 | 1,2,3,7 | 1,2,4,7 | 1,3,4,7 | 1,4,7 | 1,4 | 4, | 1,6,7 | 1,6,7,8 | 1,6 | 1,7
TDS | 0.0744 | 0.0837 | 0.0661 | 0.9389 | 0.069 | 0.0603 | 0.0466 | 0.0398 | 0.0397 | 0.3763 | 0.5237 | 0.7195 | 0.8224
Conductivity |  |  |  |  |  |  |  |  |  | 0.4343 |  |  | 
Dissolved oxygen % |  |  |  |  |  |  |  |  |  | 0.953 |  |  | 
Turbidity |  |  |  |  |  |  |  |  |  | 0.8582 |  |  | 

## Slide 9: Results
RMSE: 165.60 MAE: 114.73
RMSE: 52.26 MAE: 33.01

## Slide 10: Conclusion
To predict TDS
  Using Conductivity and precipitation has an MSE of 0.039, with a nearly perfect prediction.
  Using only known variables of precipitation and location gives an MSE of 0.38 with under and over predictions
    Is this accurate enough to use to construct the GNN?

## Slide 11: Future Work/Neural Network Uses
Developing a NN to predict river water quality from precipitation will help to develop a graphical neural network (GNN). Include other parameters such as land cover.
We need consistent data at each node to develop a well performing GNN.
Use GNN with precipitation input to determine if CSO occur, and what their impact on river water quality will be.
Use forecast precipitation to test model accuracy on forecast vs actual precipitaiton

## Slide 12: Works Cited
[1] May, R. M., Arms, S. C., Marsh, P., Bruning, E., Leeman, J. R., Goebbert, K., Thielen, J. E.,Bruick, Z., and Camron, M. D., 2024: MetPy: A Python Package for Meteorological Data. Unidata, Unidata/MetPy, doi:10.5065/D6WW7G29.
https://shap.readthedocs.io/en/latest/example_notebooks/overviews/Be%20careful%20when%20interpreting%20predictive%20models%20in%20search%20of%20causal%20insights.html
Use SHAP to determine if relationship is causal

## Slide 13
Input layer
N features
1st hidden layer
100 neurons
2nd hidden layer
60 neurons
Output layer
…
…
…